## Slide 1: 5G and the Challenges of mm-Waves
By
Jeff Fitih and Steven Jenkins

## Slide 2: Introduction to 5g

## Slide 3: WiMax Equipment

## Slide 4: London's 5G trial takes to the rooftops
​1⁄r 4 propagation over the rooftop landscape
diffraction into the "street canyon"
multipath reflection along the street
diffraction through windows, and attenuated passage through walls, into the building
reflection, diffraction, and attenuated passage through internal walls, floors and ceilings within the building

## Slide 5: LOS (Line Of Sight)
Line of sight propagation to an antenna
Impairments to line-of-sight propagation

## Slide 6: Radio horizon
Two stations not in line-of-sight may be able to communicate through an intermediate radio repeater station.
Radio wave propagation is affected by atmospheric conditions, ionospheric absorption, and the presence of obstructions, for example mountains or trees. Simple formulas that include the effect of the atmosphere give the range as:
͌ 1.23 *
͌ 3.57 *

## Slide 7: Part of the Atacama Large Millimeter Array (ALMA), a millimeter wave radio telescope

## Slide 8: 900MHz, Non-Line of Sight, Short Range, Point to Point Wireless Bridge, 8dBi Antennas, High Power, WPA/WPA2

## Slide 9: How WiMAX works in a network environment

## Slide 10: Routing
This is usually a point to point link between an active base station and a mobile station. Technologies like Opportunity Driven Multiple Access (ODMA) may have flexibility regarding which devices serve in which roles. Some types of wireless connections possess the ability to broadcast or multicast.

## Slide 11: Multicast
Multicast
Multicast can be one-to-many or many-to-many distribution.

## Slide 12: Delivery schemes
unicast delivers a message to a single specific node
broadcast delivers a message to all nodes in the network
multicast delivers a message to a group of nodes that have expressed interest in receiving the message
anycast delivers a message to any one out of a group of nodes, typically the one nearest to the source
geocast delivers a message to a group of nodes based on geographic location

## Slide 13
Unicast addressing uses a one-to-one association between a sender and destination: each destination address uniquely identifies a single receiver endpoint.
Unicast addressing

## Slide 14: Broadcasting (networking)
All-to-all communication is a computer communication method in which each sender transmits messages to all receivers within a group

## Slide 15: Anycast
Anycast is a network addressing and routing methodology in which a single destination address has multiple routing paths to two or more endpoint destinations. Routers will select the desired path on the basis of number of hops, distance, lowest cost, latency measurements or based on the least congested route.

## Slide 16: Geocast
Geocast refers to the delivery of information to a group of destinations in a network identified by their geographical locations. It is a specialized form of multicast addressing used by some routing protocols for mobile ad hoc networks.

## Slide 17: MIMO Antennas(Smart Antenna)
Ceiling Mount MIMO antennas
2.4 GHz 3 dBi Spatial Diversity MIMO Ceiling Antenna - 18in N-Female Connectors 2.4 GHz 10 dBi Dual Polarity Omnidirectional MIMO/802.11n Antenna - N-Female Connectors
Omni directional MIMO Antennas

## Slide 18: MIMO antenna
Panel MIMO Antennas
Sector MIMO Antennas
Sector MIMO Antennas
2.4 GHz 14 dBi Three Element, Dual Polarized Panel Antenna - N-Female Connectors 4.9-5.8 GHz Dual Polarity 17dBi Sector Antenna

## Slide 19: Beamforming
Beamforming or spatial filtering is a signal processing technique used in sensor arrays for directional signal transmission or reception.

## Slide 20: Trunked systems
have groups of base stations configured as repeaters. The center blocks with frequencies in this trunked block diagram each represent a base station.

## Slide 21: C-RAN Cloud/Centralized Radio Access Network
As the amount of data traffic on mobile networks continues to grow, network operators are meeting the demands by adopting Cloud/Centralized Radio Access Network architectures (C-RAN). This new approach to network architecture has two clear advantages:
Reduced CAPEX/OPEX for operators
Improved user experience through less interference

## Slide 22: C-RAN Architecture
Separating the base station into two parts, the Baseband Unit (BBU) and the Remote Radio Head (RRH), allows network operators to maintain or increase the number of network access points (RRHs), while centralizing the baseband processing functions into a “master base station”

## Slide 23: Heteregeneous network (HetNet)
Macro cells are used to provide coverage. Pico cells and micro cells are used to enhance capacity in busy areas, such as train stations, shopping malls and city centers.
Heterogeneous networks (HetNet) is a term used for modern mobile communications networks. A modern mobile communications network is comprised of a combination of different cell types and different access technologies.

## Slide 25: 5g and mm waves
Mm waves are required in order to mix 5g and existing wireless tech
Comes with many challenges:
  Propagation loss
  Penetration
  Los communication
  Multipath/nlos
  Doppler effect

## Slide 26: Propagation Loss
Propagation loss is the diluting of waves as they travel, resulting in data loss.
Loss seems to increase at higher frequencies

## Slide 27: Loss solutions
Higher loss at higher frequencies is only true for isotropic antennas
Non-isotropic antenna with Shorter wavelenths and higher frequencies have less loss
Allows for smaller antennas which means less space
Also lowers interference

## Slide 28: Penetration and LOS Communication
As mm-waves travel they have to pass through or penetrate objects in their path
Common building materials like drywall and concrete have a negative effect on LOS propogation
  Human bodies are especially a problem

## Slide 29: An Easy fix
Solving the penetration problem is simple
Separating indoor and outdoor traffic
  Different nodes should serve different sites.

## Slide 30: Multipath and NLOS
Multipath is the ability to receive a signal through more than one path
  Human bodies obstruct paths by causing shadowing
NLOS communication require equalizers
  Equalizers cause slowdown and propagation loss

## Slide 31: Angles
Wider beam width antennas solve multipathing issue
However smaller beam width antennas are much better in most other ways.
True solution requires the correct combination of wide and small beam width antennas placed at the correct angles.

## Slide 32: Doppler effect
Causes the waves to reach the destination spread out with different shift values.
This is why small beam width antennas are needed.
  Smaller starting beam means smaller spread which alleviates the issue

## Slide 33: conclusion
Propagation loss -> higher frequencies, shorter wavelengths, no isotropic antennas
Penetration and LOS communication -> separate indoor and outdoor communication
Multipath and NLOS -> correct angle for antenna with correct combination of beam width
Doppler effect -> small beam width antennas

## Slide 34: Any Questions?